## Slide 1: Custom HDL for USRP Prototyping
Winston Wang

## Slide 2: So what are USRP’s?
The USRP’s are primarily used as software defined radios. The intended use case is that consumers either
  Implement their algorithms on their PC (host) to post process data (GNU Radio)
    (very slow, underutilizes fpga, bottlenecked by the transport of samples from USRP to PC)
  Connect predefined hardware (dsp) blocks on the USRP FPGA together using the RFNOC library (RFNOC)
    Faster, but becomes significantly more complicated to integrate custom modules
This can lead to very fast development/prototyping of wireless systems/signal processing, since you can connect different processing blocks together like LEGOs
Notes: https://wiki.gnuradio.org/index.php/Main_Page
https://drive.google.com/file/d/0B6ccrJyAZaq3MTRDbmVUR0gwVU0/view?resourcekey=0-jXgCyj_rLFC8Bk699QjBiw
https://kb.ettus.com/images/e/eb/RFNoC_Wireless_at_VirginiaTech_2014_Intro.pdf

## Slide 3: So why work at the HDL level?
For some research, we want to create custom digital signal processing hardware blocks to use on the FPGAs
  Time constraints, data size constraints …
Ettus has a way for us to create our own RFNOC blocks which we could then use from the GRC flowgraphs!
  Well, do we really need the flowgraph interactivity? What’s the cost?
    Need to look under the hood

## Slide 4: How does RFNOC work?
To achieve this host side re-programmability while using digital hardware blocks, the RFNOC system specifies a communication protocol between all the blocks, handles switching and connections, and handles interfacing between RFNOC blocks and the USRP Hardware Driver (UHD)
Notes: https://kb.ettus.com/RFNoC_(UHD_3.0)

## Slide 5: Custom RFNOC?
The problem with RFNOC is that it requires wrappers for all blocks so that they can be reconfigurable. This introduces a packet based interface between blocks that is taken care by the RFNOC wrapper, but requires our modules to use an AXI interface
This introduces complexity as well as ambiguity for the engineer (how does the CHDR work? What is the latency? etc.)
If we are prototyping a device, do we need this reconfigurability? Are we OK just flashing a design to the FGPA and using it?
  A: Probably more work than its worth
Notes: https://kb.ettus.com/images/7/78/RFNoC_Wireless_at_VirginiaTech_2014_FPGA.pdf

## Slide 6: What we want
What the minimum amount of stuff we must deal with to make a prototype?
  We want an Analog front end/data converters, an FGPA, and a way to interface with a host device.
    Some radio nonideality corrections would be nice as well

## Slide 7: Towards our AFE + DC + FPGA goal
There is no customer-friendly “supported” way to get what we want.
Fortunately, the USRP host and FGPA code is all open source. We can edit the FPGA code ourselves and “hijack” the system for our goals.
This requires learning about important subsystems of the USRP and many hours of code reading/searching
Hopefully, we can condense this by explaining some major parts, and establish a framework for projects to start off of.
Notes: https://github.com/EttusResearch/uhd

## Slide 8: What is UHD?
Verilog code to handle outputs from ADC/DAC
  Processing, transport, control
C++ code to communicate with the USRP
  Transport, processing, control (again)
Notes: https://kb.ettus.com/UHD

## Slide 9: Project setup

## Slide 10: Verilog file structure
First focus on implementing the signal datapath of your modules.
  They should have a clk, reset, start signal, and data you want to read
Recommended file structure
  Make a github repo
    ex: your_project_name = OSLA
  Then make an rtl folder
  mkdir OSLA/rtl
  Make subfolders for sources
  mkdir OSLA/rtl/sources

## Slide 11: rtl/Sources
Each module has a folder
ex: source, dest, utils,…
each folder contains
  module
  testbench
  wcfg
TODO: try using packages instead of #include

## Slide 12: Matlab sim
in OSLA, make a matlab folder
Should have a subfolder testvectors, as well as your sim
testvectors will have subfolders with all of your various simulations
This is stimulus-based verification, as opposed to formal verification
  Why not formal? A: I don’t know how to
Notes: https://docs.xilinx.com/v/u/en-US/xapp199

## Slide 13: Testbench
Make a testbench (how to do this…)
To access test vectors
  $readmemb("/afs/eecs.umich.edu/spvlsi/users/wangston/OSLA/bpsk/matlab/testvectors/esn0_1/source_input.mem", tb_input);

## Slide 14: Now add UHD
I recommend making UHD a submodule of your project
Others have made their project a submodule of UHD, but that doesn’t make sense. Your project contains UHD, not the other way around. Especially if you do more than prototyping (e.g. algorithm research)
In the uhd submodule, I add branches named wangstonn/setup1, etc
  Much easier to differentiate your branches from UHD branches
git remote –v should return
Now set uhd to be the upstream
  git remote add upstream git@github.com:EttusResearch/uhd.git
  This essentially adds another repository we can pull from.
  (next slide explains why)

## Slide 15: UHD git setup continued
Ettus periodically releases UHD updates with bugfixes. (UHD 4.4, 4.5,etc)
While they do keep branches with stable releases, it is very hard to upgrade to the next release from these branches (lots of merge conflicts due to hotfixes post release).
On the other hand, master seems to be continuously updated and contains each release in its history
Because of this, we want to develop on top of upstream/master.
  to start: Git checkout –b <mybranch> upstream/master
  to update: fetch then merge upstream/master with <mybranch>
Notes: https://stackoverflow.com/questions/57272453/how-can-i-copy-commits-from-one-branch-to-another

## Slide 16: Cherry-picking
What if we developed on a stable release branch?
  We want to selectively apply all of our changes from our current branch to the upstream/master branch
  go to your history and find the range of all commits you want
  git cherry-pick <oldest commit>^..<latest commit>
This is a one-off trick! Not a permanent solution! Do this to transition to the uhd master branch.
Notes: https://stackoverflow.com/questions/46109211/cherry-picking-few-commits-from-another-branch

## Slide 17: to do:
cpp file setup

## Slide 18: Repo overview
uhd/fpga contains the Verilog used on the USRPs
  https://github.com/EttusResearch/uhd/tree/master/fpga/usrp3/top/x300
All the action happens in x300_core
  handles communication with PC, gpio, adc/dac, nonideality correction
We will insert our module here
However, there are nuances! There are many signals that we need to go through

## Slide 19
Compilation:
  https://github.com/EttusResearch/uhd/blob/master/fpga/usrp3/top/x300/Makefile.x300.inc
  Contains the makefiles needed to compile the project

## Slide 20: USRP CPP code
To build
cd uhd/host/<folder for cpp code>
mkdir build
cd build
cmake ..
make