## Slide 1: Custom HDL for USRP Prototyping
Winston Wang

## Slide 2: So what are USRP’s?
The USRP’s are primarily used as software defined radios. The intended use case is that consumers either
  Implement their algorithms on their PC (host) to post process data (GNU Radio)
    (very slow, underutilizes fpga, bottlenecked by the transport of samples from USRP to PC)
  Connect predefined hardware (dsp) blocks on the USRP FPGA together using the RFNOC library (RFNOC)
    Faster, but becomes significantly more complicated to integrate custom modules
This can lead to very fast development/prototyping of wireless systems/signal processing, since you can connect different processing blocks together like LEGOs
Notes: https://wiki.gnuradio.org/index.php/Main_Page
https://drive.google.com/file/d/0B6ccrJyAZaq3MTRDbmVUR0gwVU0/view?resourcekey=0-jXgCyj_rLFC8Bk699QjBiw
https://kb.ettus.com/images/e/eb/RFNoC_Wireless_at_VirginiaTech_2014_Intro.pdf

## Slide 3: So why work at the HDL level?
For some research, we want to create custom digital signal processing hardware blocks to use on the FPGAs
  Time constraints, data size constraints …
Ettus has a way for us to create our own RFNOC blocks which we could then use from the GRC flowgraphs!
  Well, do we really need the flowgraph interactivity? What’s the cost?
    Need to look under the hood

## Slide 4: How does RFNOC work?
To achieve this host side re-programmability while using digital hardware blocks, the RFNOC system specifies a communication protocol between all the blocks, handles switching and connections, and handles interfacing between RFNOC blocks and the USRP Hardware Driver (UHD)
Notes: https://kb.ettus.com/RFNoC_(UHD_3.0)

## Slide 5: Custom RFNOC?
The problem with RFNOC is that it requires wrappers for all blocks so that they can be reconfigurable. This introduces a packet based interface between blocks that is taken care by the RFNOC wrapper, but requires our modules to use an AXI interface
This introduces complexity as well as ambiguity for the engineer (how does the CHDR work? What is the latency? etc.)
If we are prototyping a device, do we need this reconfigurability? Are we OK just flashing a design to the FGPA and using it?
  A: Probably more work than its worth
Notes: https://kb.ettus.com/images/7/78/RFNoC_Wireless_at_VirginiaTech_2014_FPGA.pdf
https://www.gnuradio.org/grcon/grcon17/presentations/applications_and_extensions_of_gnuradio_at_APL/Jarriel-Cook-Measured-Latency-Introduced-by-RFNoC-Architecture.pdf

## Slide 6: What we want
What the minimum amount of stuff we must deal with to make a prototype?
  We want an Analog front end/data converters, an FGPA, and a way to interface with a host device.
    Some radio nonideality corrections would be nice as well

## Slide 7: Towards our AFE + DC + FPGA goal
There is no customer-friendly “supported” way to get what we want.
Fortunately, the USRP host and FGPA code is all open source. We can edit the FPGA code ourselves and “hijack” the system for our goals.
This requires learning about important subsystems of the USRP and many hours of code reading/searching
Hopefully, we can condense this by explaining some major parts, and establish a framework for projects to start from.
Notes: https://github.com/EttusResearch/uhd

## Slide 8: What is UHD?
Verilog code to handle outputs from ADC/DAC
  Processing, transport, control
C++ code to communicate with the USRP
  Transport, processing, control (again)
Notes: https://kb.ettus.com/UHD

## Slide 9: Step one: understanding the USRP architecture
Before designing any USRP system, you need to first understand the channel characteristics you are dealing with.
The USRP X310 is a motherboard that takes an analog signal, converts it, and interfaces with a computer
They connect to an RF daughterboard that handles up conversion and amplification.
This signal goes into an antenna and transmitted

## Slide 10: Daughterboards
DAC is on motherboard
Notes: https://kb.ettus.com/UBX
https://files.ettus.com/manual/page_dboards.html

## Slide 11: Bandwidth
In the X310+UBX160 setup, the daughterboard bandwidth is lower than the fpga bandwidth
https://kb.ettus.com/About_USRP_Bandwidths_and_Sampling_Rates

## Slide 12: About frequencies
What should our tx and rx frequencies be?
  Legally, must be in the ISM band (reserved for research
  2.4 GHz is attenuated by water and subject to WiFi interference
Notes: https://en.wikipedia.org/wiki/ISM_radio_band

## Slide 13: Safety
https://kb.ettus.com/X300/X310_Getting_Started_Guides

## Slide 14: GPIO
Notes: https://files.ettus.com/manual/page_gpio_api.html

## Slide 15: GPIO safety
On the fpga, a data direction register (ddr) controls whether the gpio is in input mode or output mode. There is one reg per pin
  fp_gpio_ddr = 1 -> pin = fp_gpio_out (fp_gpio_in ignored)
  fp_gpio_ddr = 0 -> fp_gpio_in = pin (fp_gpio_out ignored)
  (these names are the ones used in x300_core.v)
Problem: connecting two output gpio pin can lead to overcurrent if one is set to zero and the other is set to one. Even worse, we don’t physically know if the gpio pin is an input or output
2 solutions:
  Never directly connect gpio pins. Always connect them with a 1k resistor
  For all input pins, set fp_gpio_out = 1. This way, if we accidentally set ddr = 1, we can see by measuring the pin.

## Slide 16: Verilog reminder
‘b1 will set the first bit to one, not all of them
Use the replication operator to set a group of bits to one

## Slide 17: Streaming
Notes: https://files.ettus.com/manual/page_configuration.html

## Slide 18: Useful references
https://files.ettus.com/schematics/x300/x3xx.pdf
NI documentation
  https://kb.ettus.com/Mapping_Between_ER-USRP_and_NI-USRP_Product_Numbers
  https://www.ni.com/docs/en-US/bundle/usrp-2940-features/page/usrp-2940-feature.html
FPGA features
  https://docs.xilinx.com/v/u/en-US/7-series-product-selection-guide
  https://docs.xilinx.com/v/u/en-US/ug473_7Series_Memory_Resources
A components list:
  https://kb.ettus.com/X300/X310#Choosing_USRP_X310_vs_USRP_X300
  https://www.analog.com/media/en/technical-documentation/data-sheets/AD9146.PDF
  https://www.ti.com/lit/ds/symlink/ads62p48.pdf?ts=1697824892672&ref_url=https%253A%252F%252Fwww.google.com%252F

## Slide 19: Project setup

## Slide 20: Putty settings
Remember to save to profile

## Slide 21: vlsipool
Step 1: ssh into vlsipool-[a-z][0-9][0-9]
Step 2: vncserver :XX //establish a session on a port
Step 3: exit
Step 4: ssh –L 59XX:localhost:59XX vlsipool-[a-z][0-9][0-9] //connect the port to the tunnel
Step 5: tigervnc localhost:59XX

## Slide 22: Github
For source control, make a github repo for the project and clone it onto the afs server using https
https://docs.github.com/en/get-started/getting-started-with-git/about-remote-repositories#cloning-with-https-urls

## Slide 23: Vivado
module avail
module add Xilinx-vivado/2022.1
vivado &
First time:
Create a new project, select sources, and set the fpga
(Fpga for x310 is xc7k410tffg900-2 (active))

## Slide 24: Vivado Project
Vivado will create a TON of logs that make it hard to checkout different branches.
Create your vivado project outside of your git repo and have it linked to sources in the repo
Vivado will still add backup and sim files to your sources. These can get very large and prevent you from uploading to git. Use .gitignore to avoid these files!!!!

## Slide 25: Verilog file structure
First focus on implementing the signal datapath of your modules.
  They should have a clk, reset, start signal, and data you want to read
Recommended file structure
  Make a github repo
    ex: your_project_name = OSLA
  Then make an rtl folder
  mkdir OSLA/rtl
  Make subfolders for sources
  mkdir OSLA/rtl/sources

## Slide 26: rtl/Sources
Each module has a folder
  ex: source, dest, utils,…
each folder contains
  module hdl
  testbench
  Waveform config file .Wcfg
  Makefile.srcs (more on this later)

## Slide 27: Avoiding big file commits
Git limits storage of large files to 100 MB. This problem will only come up when you push files. To avoid having to remove a file 20 commits back, regularly push to the server.
If you do end up having a large file, you'll get the following error
remote: error: File 28b5268c3f9ea75643e90629ff9c9d093a24213d is 107.00 MB; this exceeds GitHub's file size limit of 100.00 MB
Use
git rev-list --all | while read rev; do git ls-tree -r $rev | grep 28b5268c3f9ea75643e90629ff9c9d093a24213d && echo "Found in commit $rev"; done
Find earliest commit with the file(s)
Delete the files from the current repo
Reset to that commit
commit

## Slide 28: Notes
Typically we use a sys_defs.svh file to hold the global variables. This typically doesn’t work well with usrp HDL compilation, so I’d advise using packages or parameterized values instead
Warning about parameterized modules: I once ran into a bug where the default parameter was NOT overridden by the parameter values given at instantiation. This can lead to very cryptic bugs.

## Slide 29: Multiplication

## Slide 30
module MULTIPLY;
reg signed [3:0] a = 3;
reg signed [7:0] b = 63;
wire signed [3:0] c;
wire signed [12-1:0] d;
assign c = a*b;
assign d = a*b;
initial begin
#1 $display("c= %b", c);
#1 $display("c= %b", d);
end
https://www.edaplayground.com/x/9KTz

## Slide 31: Signed unsigned multiplication
First convert to signed
module top;
bit signed [5:0] a = -1;
bit [5:0] b = 63;
bit signed [6:0] c;
initial begin
c = a*$signed({1'b0,b});
$display("%b %d",c,c);
end
Endmodule
Don’t do this, per https://docs.amd.com/v/u/en-US/ug479_7Series_DSP48E1 , design recommendations, signed bits don’t play well with dsp48E

## Slide 32
Unsigned mult is different than signed, so we have to explicitly cast to signed

## Slide 33: Fixed point operations
Subtle changes in the order of certain operations will change the result, leading to small differences between test vector and behavior
>> dec2bin_str(shift_fp(cos(2*pi*1/336),0,16,14),16,14)
ans = '0011111111111101'
>> dec2bin_str(shift_fp(-cos(2*pi*1/336),0,16,14),16,14)
ans = '1100000000000010’
The bits are merely flipped, whereas we expect a “+1”

## Slide 34: Some Verilog advice
https://nandland.com/coding-style-guidelines-for-vhdl-verilog/
https://projectf.io/posts/multiplication-fpga-dsps/
https://docs.xilinx.com/r/en-US/ug901-vivado-synthesis/Multipliers-Coding-Examples

## Slide 35: Matlab sim
in OSLA, make a matlab folder
Should have a subfolder testvectors, as well as your sim
testvectors will have subfolders with all of your various simulations
This is stimulus-based verification, as opposed to formal verification
  Why not formal? A: I don’t know how to
Notes: https://docs.xilinx.com/v/u/en-US/xapp199

## Slide 36: Testbench
Make a testbench (how to do this…)
To access test vectors
  $readmemb("/afs/eecs.umich.edu/spvlsi/users/wangston/OSLA/bpsk/matlab/testvectors/esn0_1/source_input.mem", tb_input);

## Slide 37: Simulation halting
Sometimes simulation step gets stuck at “executing analysis and compilation step”.
Solution: right click simulation and hit reset simulation

## Slide 38: IP blocks
FPGA designs use prebuilt hardware on the FPGA chip
  Furthermore there is RTL IP which is premade code that can be used to perform certain difficult tasks
    Ex: Viterbi decoding, direct digital synthesis
  This code is more reliable and efficient since it is built for the FPGA resources
To shorten development time, understand and utilize these IP’s written by Ettus and Xilinx
The only problem is that we don’t have clear models of the IP behavior, and also simulating with usrp libraries is hard (have to compile and run using a makefile) (ask demba)
Notes: https://files.ettus.com/manual/md_usrp3_simulation.html

## Slide 39: Memory
To instantiate large amounts of memory, it has to be done with a very specific port and behavioral description. Otherwise LUT’s will be synthesized and your design might run out of resources when generating the bitfile
https://docs.amd.com/r/en-US/ug901-vivado-synthesis/Single-Port-Block-RAM-with-Resettable-Data-Output-Verilog

## Slide 40: Direct Digital Synthesis
Xilinx has a DDS IP, which Ettus then wrote wrapper code for. It comes with a phase generator, but typically we perform the phase generation ourselves and just use the lookup table dds_sin_cos_lut_only
Seems IP is already instantiated, so we are stuck with the params they chose.
  Input is unsigned 24
  Output is {Q,I}, where Q and I are both signed 16 (14 frac bits, since ettus set IP to unit circle amplitude)
Notes: https://github.com/Wangstonn/ww_uhd/blob/master/fpga/usrp3/lib/rfnoc/dds_wrapper. v#L18
https://docs.xilinx.com/v/u/en-US/pg141-dds-compiler
https://github.com/dbkomma/uhd/blob/usrp_mtx_single_tone/fpga/dk_hdl/main_anc/mtx_single_tone.v

## Slide 41: Now add UHD
I recommend making UHD a submodule of your project
Others have made their project a submodule of UHD, but that doesn’t make sense. Your project contains UHD, not the other way around. Especially if you do more than prototyping (e.g. algorithm research)
In the uhd submodule, I add branches named wangstonn/setup1, etc
  Much easier to differentiate your branches from UHD branches
git remote –v should return
Now set uhd to be the upstream
  git remote add upstream git@github.com:EttusResearch/uhd.git
  This essentially adds another repository we can pull from.
  (next slide explains why)

## Slide 42: UHD git setup continued
Ettus periodically releases UHD updates with bugfixes. (UHD 4.4, 4.5,etc)
While they do keep branches with stable releases, it is very hard to upgrade to the next release from these branches (lots of merge conflicts due to hotfixes post release).
On the other hand, master seems to be continuously updated and contains each release in its history
Because of this, we want to develop on top of upstream/master.
  to start: Git checkout –b <mybranch> upstream/master
  to update: fetch then merge upstream/master with <mybranch>
See the cherrypicking slide if you didn’t do this
Notes: https://stackoverflow.com/questions/57272453/how-can-i-copy-commits-from-one-branch-to-another

## Slide 43: Installing UHD to host computers (HSK laptops only)
First, run ./uhd_find_devices
git clone <link to your uhd repo>
cd <uhd-repo-path>/host
If the uhd version you want is installed, see below. Else, go to next slide
Then append the following two lines to .bashrc (this allows us to choose which uhd version to use if there are multiple)
export LD_LIBRARY_PATH=$HOME/.local/lib/uhd-4.5/lib:$LD_LIBRARY_PATH
export PATH="$HOME/.local/lib/uhd-4.5/bin:$PATH“
After this, you should be able to run uhd_find devices and see the version
Notes: Modified instructions
https://files.ettus.com/manual/page_build_guide.html
https://stackoverflow.com/questions/480764/linux-error-while-loading-shared-libraries-cannot-open-shared-object-file-no-s

## Slide 44: Custom UHD installs
If the correct version of uhd isn’t installed, now that we have loaded the c++ code from the repo, we need to install so that we can use the functions. For example, if using uhd-4.5:
mkdir build
cd build
cmake -DCMAKE_INSTALL_PREFIX=$HOME/.local/lib/uhd-4.5 ../
make
make test
sudo make install
sudo ldconfig

## Slide 45: Ethernet connection (HSK laptops)
HSK laptops have one ethernet card (demba check?)
Run uhd_usrp_probe
If nothing shows up, go to settings>network>wired>add new connection
Give the new connection a name (USRP4343, etc), then on ipv4, select manual and input the ip and subnet mask 255.255.255.0
Select connect automatically if desired
Now uhd_usrp_probe should successfully identify the usrp

## Slide 46: Repo overview
uhd/fpga contains the Verilog used on the USRPs
  https://github.com/EttusResearch/uhd/tree/master/fpga/usrp3/top/x300
All the action happens in x300_core
  handles communication with PC, gpio, adc/dac, nonideality correction
We will insert our module here
However, there are nuances! There are many signals that we need to go through

## Slide 47: Cherry-picking
This is for fixing repos (don’t do this for setup)
What if we developed on a stable release branch?
  We want to selectively apply all of our changes from our current branch to the upstream/master branch
  go to your history and find the range of all commits you want
  git cherry-pick <oldest commit>^..<latest commit>
This is a one-off trick! Not a permanent solution! Do this to transition to the uhd master branch.
Notes: https://stackoverflow.com/questions/46109211/cherry-picking-few-commits-from-another-branch

## Slide 48: Preface
for .sh files, run using . <filename>.sh
for c++ files, run using ./<filename>

## Slide 49: HDL Makefile setup
To compile the HDL, the makefile needs to know which files are needed. This is done by reading makefile.srcs files, which contain a list of all hdl code we use.
In each module folder, add a Makefile.srcs file that
  Adds all utility files
  Adds the full paths to each of the hdl files
In the top module folder Makefile, add all the files that are being used. To add this Makefile, include the path to the Makefile.srcs and append the path string to DESIGN_SRCS
https://github.com/Wangstonn/ww_uhd/blob/osla-bpsk-4.5/fpga/usrp3/top/x300/Makefile.x300.inc
Notes: https://github.com/EttusResearch/uhd/blob/master/fpga/usrp3/top/x300/Makefile.x300.inc

## Slide 50: Compilation/bitfile generation
module load python/3.8.5
. ./setupenv.sh --vivado-path /usr/caen/xilinx/2021.1/Vivado/
make X310_HG
vivado path will change based on uhd version
https://github.com/Wangstonn/ww_uhd/blob/osla-bpsk-4.5/fpga/usrp3/top/x300/vlsi_make.sh
Move the files from the untracked build folder and commit+push to git
mv build/usrp_x310_fpga_HG.bit ./usrp_x310_fpga_HG.bit
Pull on the lab computer and run
uhd_image_loader --args type=x300 addr=192.168.110.2 --fpga-path usrp_x310_fpga_HG.bit
IP addresses and reservation are found here: https://docs.google.com/spreadsheets/d/1B6xLjOiw-5AcmWQ2GNcWTHVfxSufC8P4PqGfJjSeS0I/edit#gid=0
Notes: https://github.com/Wangstonn/ww_uhd/blob/osla-bpsk-4.5/fpga/usrp3/top/x300/vlsi_make.sh
usrp_load.sh
mv_bitfile.sh

## Slide 51: Structuring a C++ project
Your code should be organized into folders that contain functions, their header, and a unit test.
project_folder/
│
├── main.cpp // Contains the main program logic
└── src/ // Folder containing source files
├── functions.cpp // Implementation of functions
├── functions.h // Header file declaring functions
└── tests.cpp // File for testing functions
These functions can be further grouped into libraries
Notes: https://api.csswg.org/bikeshed/?force=1&url=https://raw.githubusercontent.com/vector-of-bool/pitchfork/develop/data/spec.bs

## Slide 52: Header file
//Include guards to prevent repeated definition
#ifndef CROSS_CORRELATION_H
#define CROSS_CORRELATION_H
//libraries needed to be included in function c++ file
#include <vector>
#include <complex>
//function prototypes
std::tuple<std::vector<std::complex<double>>, std::vector<int>> crossCorrelationComplex(const std::vector<std::complex<double>>& x, const std::vector<std::complex<double>>& y);
#endif // CROSS_CORRELATION_H

## Slide 53: CMake
Up to now, you probably used an IDE to compile c++ files. When compiling on a linux server, the command used is
g++ -o test xcorr_slow.test.cpp
What happens is you have a function in a separate file? Then c++ must compile both and link them
g++ -o test xcorr_slow.test.cpp xcorr_slow.cpp
With many function and many files. This can quickly become too complex.
CMake is a build tool that uses CMakeLists.txt to record dependencies and allow us to build larger c++ executables
Notes: https://stackoverflow.com/questions/3202136/using-g-to-compile-multiple-cpp-and-h-files

## Slide 54: CMakeLists.txt files
Each folder will have a CMakeLists.txt
root
|- MainProject
| |- main.cpp
| |- CMakeLists.txt
| |- src
| | |- xcorr
| | | |- xcorr.h
| | | |- xcorr.cpp
| | | |- test.cpp
| | | '- CMakeLists.txt
| | '- fft
| | |- fft.h
| | |- fft.cpp
| | |- test.cpp
| | '- CMakeLists.txt
Notes: https://stackoverflow.com/questions/2360734/whats-a-good-directory-structure-for-larger-c-projects-using-makefile
https://www.open-std.org/jtc1/sc22/wg21/docs/papers/2018/p1204r0.html
https://stackoverflow.com/questions/8304190/cmake-with-include-and-source-paths-basic-setup
https://gitlab.kitware.com/cmake/community/-/wikis/doc/cmake/Useful-Variables
https://stackoverflow.com/questions/4506193/what-are-the-dusty-corners-a-newcomer-to-cmake-will-want-to-know
https://cmake.org/cmake/help/latest/guide/tutorial/Adding%20a%20Library.html

## Slide 55: CMake function overview
project(): determines the name of the project
add_subdirectory(): adds subdirectories containing other cmakelists
add_executable(): creates the executable from the cpp file
target_link_libraries(MainExecutable XCorr FFT): links libraries (defined in subdirectory cmakelists.txt) to the main executable
add_library(XCorr
xcorr.cpp
xcorr.h #unit test file missing since we don’t want to link it to mainexec
) # Create a library from sources in subdirectory folder

## Slide 56: CMake config
cd uhd/host/<folder for c++ code>
mkdir build
cd build
cmake -DCMAKE_INSTALL_PREFIX=$HOME/.local/lib/uhd-4.5 ../
make
Inside build will be the executable (execute using ./build_exec)
Note that your executable will be in project/build. This is important when accessing files using relative path, since itll be different than the location of the cpp file
std::ifstream if_file("../../../matlab/mlsr/preamble.mem");

## Slide 57: USRP CPP code build
use VScode to ssh into aa machine
Make a folder in host, copying https://github.com/EttusResearch/uhd/tree/master/host/examples/init_usrp
modify the CMakelists.txt to run your c++ file instead
Configure cmake (prev slide)
./your_build --tx-args "type=x300,addr=192.168.110.2" --rx-args "type=x300,addr=192.168.110.2"

## Slide 58: USRP Processing Delay
USRP Loopback Test
USRP Processing Delay must be accounted for in implementation for timing
Get USRP TX and RX processing delay
Processing Delay contains ADC, DAC, and Analog Frontend processing times.
An estimated constant delay was measured from USRP. Similar results from an additional USRPS with same wire.
Wired Cable used to connect. Wire Length is about 8 inches.
RX
USRP
TX

## Slide 59: USRP Processing Delay
Estimated Processing Delay = 119 samples at 200M = 0.595 us
Processing includes TX path, RX path and Wire length.
Wire Length = 8 inches

## Slide 60: Antennas
Make sure antennas are aligned
Check antenna datasheets and make sure they are compatible with your tx frequency
Notes: https://www.everythingrf.com/rf-calculators/antenna-near-field-distance-calculator
https://www.antenna-theory.com/basics/radpattern.php
https://kb.ettus.com/images/2/2b/ettus_research_vert900_datasheet.pdf

## Slide 61: Channel characterization
8 inch antenna
2 meter distance
915 MHz
Far field measurement

## Slide 62: Range
How does our SNR vary with distance?
Friis’ equation (far field)

## Slide 63: Receiver sensitivity
First, calculate the voltage seen at the ADC
Measured gain from antenna to adc
Convert to power using 50 Ohm resistor
Notes: https://e2e.ti.com/blogs_/archives/b/precisionhub/posts/it-s-in-the-math-how-to-convert-adc-code-to-a-voltage-part-1

## Slide 64: Flicker noise
Flicker noise is colored noise around DC. This forces us to receive signals at a digital IF frequency
595.3 kHz
Peak flicker is around 3dB higher than noise floor
Matched filter frequency response (after IF downconversion)

## Slide 65: Low IF design
Flicker corner frequency around 100 kHz
Choose a low IF frequency above 400 kHz
Single sided signalling requires transmitting a complex exponential
Flicker Corner Frequency

## Slide 66: DC offset
Idea: change alpha so that roll off is faster
https://github.com/Wangstonn/ww_uhd/blob/master/fpga/usrp3/lib/dsp/rx_dcoffset.v#L54
https://files.ettus.com/manual/page_calibration.html
https://files.ettus.com/manual/classuhd_1_1usrp_1_1multi__usrp.html#a7beb49c1a04a81b3e7569db482453746

## Slide 67: Gain control
Increasing rx gain will not increase the measured noise and signal equally. This is because at low rx-gain, the noise is dominated by the noise figure at the output of the LNA. As rx-gain rises, eventually received noise dominates.
Notes: rx_gain = [0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 10, 11, 12, 13, 14, 15, 16, 17, 18, 19, 20, 21, 22, 23, 24, 25, 26, 27, 28, 29, 30];
var = [29.4913, 29.385, 29.5782, 28.9859, 29.8356, 30.0203, 29.3961, 30.4743, 30.554, 30.9916, 31.4724, 32.3447, 32.9011, 34.0835, 35.9594, 36.9853, 39.5754, 41.4779, 45.2277, 48.711, 54.9174, 60.9974, 69.2489, 78.4937, 92.0707, 106.649, 127.236, 149.659, 182.996, 221.991, 269.37];

## Slide 68: Synchronization
https://www.youtube.com/watch?v=6TOU0f039g8
https://files.ettus.com/manual/page_sync.html
https://www.mail-archive.com/usrp-users@lists.ettus.com/msg14581.html

## Slide 69: RFNOC library
/afs/eecs.umich.edu/spvlsi/users/wangston/OSLA/bpsk/ww_uhd/fpga/usrp3/lib/rfnoc/moving_sum.v:8

## Slide 70: Useful USRP settings
https://files.ettus.com/manual/classuhd_1_1usrp_1_1multi__usrp.html#a41cc3c774451d0a2c5f69cd8df0f9f06
https://files.ettus.com/manual/page_dboards.html
  Daughterboard setting limits

## Slide 71: RF tuning and front end settling time
https://files.ettus.com/manual/page_general.html

## Slide 72: Working with USRP c++ code
https://files.ettus.com/manual/classuhd_1_1usrp_1_1multi__usrp.html#a38b10a6bd2128b3810da229c60b31aa1
https://files.ettus.com/manual/page_configuration.html

## Slide 73: Commanding the USRP’s
https://files.ettus.com/manual/page_usrp_x3x0.html

## Slide 74: Loopback params
Loopback, 8 inch wire, 30dB attenuator (tx/rx gain = 0)
Setting TX Freq: 2400.000000 MHz..
D_hat= 119, EsN0= 14.8833, h_hat : abs= 0.439122 arg= 3.12618
Attenuators dont affect delay
rx/tx gain dont affect delay
freq doesnt affect delay

## Slide 75: gpio regs
https://www.youtube.com/watch?v=ppD06ZETnek
https://events.gnuradio.org/event/18/contributions/234/attachments/74/186/GPIOs%20on%20USRPs.pdf

## Slide 76: General useful information
https://www.youtube.com/watch?app=desktop&v=PNMOwhEHE6w
https://www.youtube.com/watch?v=wqKNUXDdIvU&t=1811s https://en.wikipedia.org/wiki/Stochastic_resonance
https://www.youtube.com/watch?v=FxciG7nW-J0

## Slide 77: Nonideality correction
fe_control sits between x300 and adc (CHECK)
https://github.com/Wangstonn/ww_uhd/blob/master/fpga/usrp3/lib/control/fe_control.v#L14
Performs DC offset correction, etc
https://github.com/Wangstonn/ww_uhd/blob/master/fpga/usrp3/lib/rfnoc/blocks/rfnoc_block_radio/tx_frontend_gen3.v#L8

## Slide 78: Debug advice
(* dont_touch = "true" , mark_debug = "true" *) logic fb_o_ctr_r
(* DONT_TOUCH = "yes" *) dest dest_dut( )
Notes: https://docs.xilinx.com/r/2021.1-English/ug1387-acap-hardware-ip-platform-dev-methodology/Synthesis-Attributes
https://docs.xilinx.com/r/en-US/ug901-vivado-synthesis/DONT_TOUCH

## Slide 79: Frequency tuning
https://files.ettus.com/manual/page_general.html